## Slide 1: Flood extent mapping

## Slide 2: What solution is best suited for my case?
Terrain Type | Type of Flood Event |  |  |  |  |  | Available Imagery
 | Flash Flood |  | Seasonal Flood (< 2 months of rain) |  | Seasonal Flood (> 2 months of rain) |  | 
 | S1 | S2 | S1 | S2 | S1 | S2 | 
not specific |  |  | AnomalyD |  |  |  | Every analysis is limited by data availability and data quality. While radar data is best suited for analysis floods (because it can penetrate clouds during rainy seasons), sometimes the data is not readily available and we need to utilize optical data, or combine the two data types.
wetlands |  |  | NDFI |  | NDFVI |  | 
mountainous | AnomalyD | SVM |  |  |  |  | 
urban |  |  |  | MNDWI | Data Fusion | Data Fusion | 
Data Type | Method | Alias
S1 | Anomaly Detection | AnomalyD
S1 | NDFI | NDFI
S1 | NDFVI | NDFVI
S2 | SVM | SVM
S2 | MNDWI | MNDWI
S1 + S2 | S1 NDFI + S2 MNDWI | Data Fusion

## Slide 3: S1 – Anomaly Detection
This approach takes the advantage of using stack of images for the pre- and post- event by using their statistics for detecting the flood as an anomaly
Most suitable use cases: flood events where the flood area can be clearly detected from the surrounding environment
Niger floods
(summer 2020)

## Slide 4: S1 – NDFI
This approach is based on this paper from 2018 (https://doi.org/10.1016/j.rse.2018.03.006) –while it is based as well in the SAR backscatter statistics , it defines a Normalized Difference Flood Index, applicable to any X- and C- band SAR sensors. The typical value for this threshold is 0.7, but the authors does not suggest to go lower than 0.6
Most suitable use cases: flat terrains with low vegetation prone to recurrent seasonal floods, wetlands
Niger floods
(summer 2020)
NDFI= (mean
(reference)-min⁡(reference+
flood))/
(mean(
reference)+min⁡(reference+flood))

## Slide 5: S1 – NDFVI
This index detects water in shallow vegetation, and its suggested threshold is 0.75. In some instances, it is worth combining the 2 indexes, depending on the terrain of the AOI.
Most suitable use cases: we recommend using this index when the flooded areas occur in fields with shallow vegetation
SSD floods
(summer 2020)
NDFVI= ( max⁡(reference+ flood)-mean(reference)) /
(max⁡(
reference+
flood)+mean (reference) )

## Slide 6: S2 - SVM

## Slide 7: S2 - MNDWI

## Slide 8: Data Fusion ( S1 + S2 )